## Slide 1: Machine-Level Programming II: Arithmetic & Control Books: Programming from the ground up (Chapter 1-3) Computer Systems (Chapter 3)

## Slide 2: Today
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
While loops

## Slide 3: Complete Memory Addressing Modes
Most General Form
D(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]+ D]
  D: Constant “displacement” 1, 2, or 4 bytes
  Rb: Base register: Any of 8 integer registers
  Ri: Index register: Any, except for %esp
    Unlikely you’d use %ebp, either
  S: Scale: 1, 2, 4, or 8 (why these numbers?)
Special Cases
(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]]
D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D]
(Rb,Ri,S) Mem[Reg[Rb]+S*Reg[Ri]]

## Slide 4: Address Computation Instruction
leal Src,Dest
  Src is address mode expression
  Set Dest to address denoted by expression
Uses
  Computing addresses without a memory reference
    E.g., translation of p = &x[i];
  Computing arithmetic expressions of the form x + k*y
    k = 1, 2, 4, or 8
Example
int mul12(int x)
{
return x*12;
}
leal (%eax,%eax,2), %eax ;t <- x+x*2
sall $2, %eax ;return t<<2
Converted to ASM by compiler:

## Slide 5: Today
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
While loops

## Slide 6: Some Arithmetic Operations
Two Operand Instructions:
  Format Computation
    addl Src,Dest Dest = Dest + Src
    subl Src,Dest Dest = Dest  Src
    imull Src,Dest Dest = Dest * Src
    sall Src,Dest Dest = Dest << Src Also called shll
    sarl Src,Dest Dest = Dest >> Src Arithmetic
    shrl Src,Dest Dest = Dest >> Src Logical
    xorl Src,Dest Dest = Dest ^ Src
    andl Src,Dest Dest = Dest & Src
    orl Src,Dest Dest = Dest | Src
Watch out for argument order!

## Slide 7: Some Arithmetic Operations
One Operand Instructions
    incl Dest Dest = Dest + 1
    decl Dest Dest = Dest  1
    negl Dest Dest =  Dest
    notl Dest Dest = ~Dest
See book for more instructions

## Slide 8: Arithmetic Expression Example
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
arith:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %ecx
movl 12(%ebp), %edx
leal (%edx,%edx,2), %eax
sall $4, %eax
leal 4(%ecx,%eax), %eax
addl %ecx, %edx
addl 16(%ebp), %edx
imull %edx, %eax
popl %ebp
ret
Body
Set
Up
Finish

## Slide 9: Understanding arith
 | •
 | •
 | •
16 | z
12 | y
8 | x
4 | Rtn Addr
0 | Old %ebp
movl 8(%ebp), %ecx
movl 12(%ebp), %edx
leal (%edx,%edx,2), %eax
sall $4, %eax
leal 4(%ecx,%eax), %eax
addl %ecx, %edx
addl 16(%ebp), %edx
imull %edx, %eax
%ebp
Offset
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}

## Slide 10: Understanding arith
 | •
 | •
 | •
16 | z
12 | y
8 | x
4 | Rtn Addr
0 | Old %ebp
%ebp
Offset
Stack
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}
movl 8(%ebp), %ecx # ecx = x
movl 12(%ebp), %edx # edx = y
leal (%edx,%edx,2), %eax # eax = y*3
sall $4, %eax # eax *= 16 (t4)
leal 4(%ecx,%eax), %eax # eax = t4 +x+4 (t5)
addl %ecx, %edx # edx = x+y (t1)
addl 16(%ebp), %edx # edx += z (t2)
imull %edx, %eax # eax = t2 * t5 (rval)

## Slide 11: Observations about arith
  Instructions in different order from C code
  Some expressions require multiple instructions
  Some instructions cover multiple expressions
  Get exact same code when compile:
  (x+y+z)*(x+4+48*y)
movl 8(%ebp), %ecx # ecx = x
movl 12(%ebp), %edx # edx = y
leal (%edx,%edx,2), %eax # eax = y*3
sall $4, %eax # eax *= 16 (t4)
leal 4(%ecx,%eax), %eax # eax = t4 +x+4 (t5)
addl %ecx, %edx # edx = x+y (t1)
addl 16(%ebp), %edx # edx += z (t2)
imull %edx, %eax # eax = t2 * t5 (rval)
int arith(int x, int y, int z)
{
int t1 = x+y;
int t2 = z+t1;
int t3 = x+4;
int t4 = y * 48;
int t5 = t3 + t4;
int rval = t2 * t5;
return rval;
}

## Slide 12: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)

## Slide 13: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)

## Slide 14: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)

## Slide 15: Another Example
int logical(int x, int y)
{
int t1 = x^y;
int t2 = t1 >> 17;
int mask = (1<<13) - 7;
int rval = t2 & mask;
return rval;
}
logical:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
xorl 8(%ebp),%eax
sarl $17,%eax
andl $8185,%eax
popl %ebp
ret
Body
Set
Up
Finish
movl 12(%ebp),%eax # eax = y
xorl 8(%ebp),%eax # eax = x^y (t1)
sarl $17,%eax # eax = t1>>17 (t2)
andl $8185,%eax # eax = t2 & mask (rval)
213 = 8192, 213 – 7 = 8185

## Slide 16: Today
Complete addressing mode, address computation (leal)
Arithmetic operations
Control: Condition codes
Conditional branches
Loops

## Slide 17: Processor State (IA32, Partial)
Information about currently executing program
  Temporary data ( %eax, … )
  Location of runtime stack ( %ebp,%esp )
  Location of current code control point ( %eip, … )
  Status of recent tests ( CF, ZF, SF, OF )
%eip
General purpose
registers
Current stack top
Current stack frame
Instruction pointer
CF
ZF
SF
OF
Condition codes
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp

## Slide 18: Condition Codes (Implicit Setting)
Single bit registers
  CF Carry Flag (for unsigned) SF Sign Flag (for signed)
  ZF Zero Flag OF Overflow Flag (for signed)
Implicitly set (think of it as side effect) by arithmetic operations
  Example: addl/addq Src,Dest ↔ t = a+b
  CF set if carry out from most significant bit (unsigned overflow)
  ZF set if t == 0
  SF set if t < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b>0 && t<0) || (a<0 && b<0 && t>=0)
Not set by lea instruction

## Slide 19: Which flags are set? (see GDB view)
#include <limits.h>
int sum(int x, int y) {
int t = x + y;
return t;
}
int main() {
return sum(1, INT_MAX);
}
SF – because t is negative
OF – because overflow in add
Notes: Ignore other flags for this lecture.

## Slide 20: Zero flag
#include <limits.h>
int sum(int x, int y) {
int t = x + y;
return t;
}
int main() {
return sum(0, 0);
}
ZF – because t is zero

## Slide 21: Carry flag
#include <limits.h>
unsigned int sum(unsigned int x, unsigned int y) {
int t = x + y;
return t;
}
int main() {
return sum(2, UINT_MAX);
}
CF – because x+y overflows

## Slide 22: Condition Codes (Explicit Setting: Compare)
Explicit Setting by Compare Instruction
  cmpl/cmpq Src2, Src1
  cmpl b,a like computing a-b without setting destination
  CF set if carry out from most significant bit (used for unsigned comparisons)
  ZF set if a == b
  SF set if (a-b) < 0 (as signed)
  OF set if two’s-complement (signed) overflow (a>0 && b<0 && (a-b)<0) || (a<0 && b>0 && (a-b)>0)

## Slide 23: Zero flag (comparison)
ZF – because x == y
int max(int x, int y) {
if(x <= y) {
return y;
} else {
return x;
}
}
int main(){
return max(2, 2);
}

## Slide 24: Sign flag (comparison)
int max(int x, int y) {
if(x <= y) {
return y;
} else {
return x;
}
}
int main(){
return max(1, 2);
}
SF – because 1-2 <= 0 (see disass in the next slide)
CF – because 1-2 <= 0

## Slide 25: Disassembly of max
eax = 1
0xc(%ebp) = 2
cmp 2, 1
or 1-2 <= 0

## Slide 26: Condition Codes (Explicit Setting: Test)
Explicit Setting by Test instruction
  testl/testq Src2, Src1 testl b,a like computing a&b without setting destination
  Sets condition codes based on value of Src1 & Src2
  ZF set when a&b == 0
  SF set when a&b < 0

## Slide 27: Zero flag (Condition code)
int main(){
int x = 1, y = 2;
if(x & y) return 1;
else return 0;
}
ZF – because 1&2 == 0 (see disass in the next slide)

## Slide 28: Disass for zero flag demo
test will not modify eax

## Slide 29: Sign flag (Condition code a & b < 0)
int main(){
int x = -1, y = -2;
if(x & y) return 1;
else return 0;
}
SF – because -1&-2 == -2 < 0

## Slide 30: Reading Condition Codes
SetX Instructions
  Set single byte based on combinations of condition codes
SetX | Condition | Description
sete | ZF | Equal / Zero
setne | ~ZF | Not Equal / Not Zero
sets | SF | Negative
setns | ~SF | Nonnegative
setg | ~(SF^OF)&~ZF | Greater (Signed)
setge | ~(SF^OF) | Greater or Equal (Signed)
setl | (SF^OF) | Less (Signed)
setle | (SF^OF)¦ZF | Less or Equal (Signed)
seta | ~CF&~ZF | Above (unsigned)
setb | CF | Below (unsigned)

## Slide 31: Reading Condition Codes (Cont.)
movl 12(%ebp),%eax # eax = y
cmpl %eax,8(%ebp) # Compare x : y
setg %al # al = x > y
movzbl %al,%eax # Zero rest of %eax
SetX Instructions:
  Set single byte based on combination of condition codes
One of 8 addressable byte registers
  Does not alter remaining 3 bytes
  Typically use movzbl to finish job
int gt (int x, int y)
{
return x > y;
}
Body
%eax | %ah | %al
%ecx | %ch | %cl
%edx | %dh | %dl
%ebx | %bh | %bl
%esi |  | 
%edi |  | 
%esp |  | 
%ebp |  | 

## Slide 32: Reading Condition Codes: x86-64
int gt (long x, long y)
{
return x > y;
}
cmpl %esi, %edi
setg %al
movzbl %al, %eax
Bodies
long lgt (long x, long y)
{
return x > y;
}
SetX Instructions:
  Set single byte based on combination of condition codes
  Does not alter remaining 3 bytes
Is %rax zero?
Yes: 32-bit instructions set high order 32 bits to 0!
cmpq %rsi, %rdi
setg %al
movzbl %al, %eax

## Slide 33: Today
Complete addressing mode, address computation (leal)
Arithmetic operations
x86-64
Control: Condition codes
Conditional branches & Moves
Loops

## Slide 34: Jumping
jX Instructions
  Jump to different part of code depending on condition codes
jX | Condition | Description
jmp | 1 | Unconditional
je | ZF | Equal / Zero
jne | ~ZF | Not Equal / Not Zero
js | SF | Negative
jns | ~SF | Nonnegative
jg | ~(SF^OF)&~ZF | Greater (Signed)
jge | ~(SF^OF) | Greater or Equal (Signed)
jl | (SF^OF) | Less (Signed)
jle | (SF^OF)¦ZF | Less or Equal (Signed)
ja | ~CF&~ZF | Above (unsigned)
jb | CF | Below (unsigned)

## Slide 35: Conditional Branch Example
int absdiff(int x, int y)
{
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 36: Conditional Branch Example (Cont.)
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
C allows “goto” as means of transferring control
  Closer to machine-level programming style
Generally considered bad coding style
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 37: Conditional Branch Example (Cont.)
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 38: Conditional Branch Example (Cont.)
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 39: Conditional Branch Example (Cont.)
int goto_ad(int x, int y)
{
int result;
if (x <= y) goto Else;
result = x-y;
goto Exit;
Else:
result = y-x;
Exit:
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L6
subl %eax, %edx
movl %edx, %eax
jmp .L7
.L6:
subl %edx, %eax
.L7:
popl %ebp
ret
Body1
Setup
Finish
Body2b
Body2a

## Slide 40: General Conditional Expression Translation
C Code
val = Test ? Then_Expr : Else_Expr;
Goto Version
nt = !Test;
if (nt) goto Else;
val = Then_Expr;
goto Done;
Else:
val = Else_Expr;
Done:
. . .
  Test is expression returning integer
    = 0 interpreted as false
    ≠ 0 interpreted as true
  Create separate code regions for then & else expressions
  Execute appropriate one
val = x>y ? x-y : y-x;

## Slide 41: Using Conditional Moves
C Code
val = Test
? Then_Expr
: Else_Expr;
Goto Version
tval = Then_Expr;
result = Else_Expr;
t = Test;
if (t) result = tval;
return result;
Conditional Move Instructions
  Instruction supports:
    if (Test) Dest  Src
  Supported in post-1995 x86 processors
  GCC does not always use them
    Wants to preserve compatibility with ancient processors
    Enabled for x86-64
    Use switch –march=686 for IA32
Why?
  Branches are very disruptive to instruction flow through pipelines
  Conditional move do not require control transfer

## Slide 42: Conditional Move Example: x86-64
int absdiff(int x, int y) {
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
movl %edi, %edx
subl %esi, %edx # tval = x-y
movl %esi, %eax
subl %edi, %eax # result = y-x
cmpl %esi, %edi # Compare x:y
cmovg %edx, %eax # If >, result = tval
ret
x in %edi
y in %esi

## Slide 43: Bad Cases for Conditional Move
Expensive Computations
Both values get computed
Only makes sense when computations are very simple
val = Test(x) ? Hard1(x) : Hard2(x);
Risky Computations
Both values get computed
May have undesirable effects
val = p ? *p : 0;
Computations with side effects
Both values get computed
Must be side-effect free
val = x > 0 ? x*=7 : x+=3;

## Slide 44: Today
Complete addressing mode, address computation (leal)
Arithmetic operations
x86-64
Control: Condition codes
Conditional branches and moves
Loops

## Slide 45: “Do-While” Loop Example
C Code
int pcount_do(unsigned x) {
int result = 0;
do {
result += x & 0x1;
x >>= 1;
} while (x);
return result;
}
Goto Version
int pcount_do(unsigned x)
{
int result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
return result;
}
Count number of 1’s in argument x (“popcount”)
Use conditional branch to either continue looping or to exit loop

## Slide 46: “Do-While” Loop Compilation
Goto Version
Registers:
  %edx x
  %ecx result
movl $0, %ecx # result = 0
.L2: # loop:
movl %edx, %eax
andl $1, %eax # t = x & 1
addl %eax, %ecx # result += t
shrl %edx # x >>= 1
jne .L2 # If !0, goto loop
int pcount_do(unsigned x) {
int result = 0;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
return result;
}

## Slide 47: General “Do-While” Translation
C Code
do
Body
while (Test);
Goto Version
loop:
Body
if (Test)
goto loop
Body:
Test returns integer
  = 0 interpreted as false
  ≠ 0 interpreted as true
{
Statement1;
Statement2;
…
Statementn;
}

## Slide 48: “While” Loop Example
C Code
Goto Version
int pcount_while(unsigned x) {
int result = 0;
while (x) {
result += x & 0x1;
x >>= 1;
}
return result;
}
int pcount_do(unsigned x) {
int result = 0;
if (!x) goto done;
loop:
result += x & 0x1;
x >>= 1;
if (x)
goto loop;
done:
return result;
}

## Slide 49: General “While” Translation
While version
while (Test)
Body
Do-While Version
if (!Test)
goto done;
do
Body
while(Test);
done:
Goto Version
if (!Test)
goto done;
loop:
Body
if (Test)
goto loop;
done:

## Slide 50: “For” Loop Example
C Code
Is this code equivalent to other versions?
#define WSIZE 8*sizeof(int)
int pcount_for(unsigned x) {
int i;
int result = 0;
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
return result;
}

## Slide 51: “For” Loop Form
for (Init; Test; Update )
Body
General Form
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
i = 0
i < WSIZE
i++
{
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
Init
Test
Update
Body

## Slide 52: “For” Loop  While Loop
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version

## Slide 53: “For” Loop  …  Goto
for (Init; Test; Update )
Body
For Version
Init;
while (Test ) {
Body
Update;
}
While Version
Init;
if (!Test)
goto done;
do
Body
Update
while(Test);
done:
Init;
if (!Test)
goto done;
loop:
Body
Update
if (Test)
goto loop;
done:

## Slide 54: “For” Loop Conversion Example
C Code
Initial test can be optimized away
#define WSIZE 8*sizeof(int)
int pcount_for(unsigned x) {
int i;
int result = 0;
for (i = 0; i < WSIZE; i++) {
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
return result;
}
Goto Version
int pcount_for_gt(unsigned x) {
int i;
int result = 0;
i = 0;
if (!(i < WSIZE))
goto done;
loop:
{
unsigned mask = 1 << i;
result += (x & mask) != 0;
}
i++;
if (i < WSIZE)
goto loop;
done:
return result;
}
Init
!Test
Body
Update
Test

## Slide 55: Summarizing
C Control
  if-then-else
  do-while
  while, for
Assembler Control
  Conditional jump
  Conditional move
  Indirect jump
  Compiler generates code sequence to implement more complex control