## Slide 1: Switch Statement, Arrays, and Structs 5th Lecture

## Slide 2: Today
Switch Statement
Arrays
Structures

## Slide 3: Switch Statement Example
Multiple case labels
  Here: 5 & 6
Fall through cases
  Here: 2
Missing cases
  Here: 4
long switch_eg
(long x, long y, long z)
{
long w = 1;
switch(x) {
case 1:
w = y*z;
break;
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
case 5:
case 6:
w -= z;
break;
default:
w = 2;
}
return w;
}

## Slide 4: Jump Table Structure
Code Block
0
Targ0:
Code Block
1
Targ1:
Code Block
2
Targ2:
Code Block
n–1
Targn-1:
•
•
•
Targ0
Targ1
Targ2
Targn-1
•
•
•
jtab:
target = JTab[x];
goto *target;
switch(x) {
case val_0:
Block 0
case val_1:
Block 1
• • •
case val_n-1:
Block n–1
}
Switch Form
Approximate Translation
Jump Table
Jump Targets

## Slide 5: Switch Statement Example (IA32)
Setup:
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
switch_eg:
pushl %ebp # Setup
movl %esp, %ebp # Setup
movl 8(%ebp), %eax # %eax = x
cmpl $6, %eax # Compare x:6
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]
What range of values takes default?
Note that w not initialized here

## Slide 6: Switch Statement Example (IA32)
long switch_eg(long x, long y, long z)
{
long w = 1;
switch(x) {
. . .
}
return w;
}
Indirect jump
Jump table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6
Setup:
switch_eg:
pushl %ebp # Setup
movl %esp, %ebp # Setup
movl 8(%ebp), %eax # eax = x
cmpl $6, %eax # Compare x:6
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]

## Slide 7: Assembly Setup Explanation
Table Structure
  Each target requires 4 bytes
  Base address at .L7
Jumping
  Direct: jmp .L2
  Jump target is denoted by label .L2
  Indirect: jmp *.L7(,%eax,4)
  Start of jump table: .L7
  Must scale by factor of 4 (labels have 32-bits = 4 Bytes on IA32)
  Fetch target from effective Address .L7 + eax*4
    Only for 0 ≤ x ≤ 6
Jump table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6

## Slide 8: Jump Table
.section .rodata
.align 4
.L7:
.long .L2 # x = 0
.long .L3 # x = 1
.long .L4 # x = 2
.long .L5 # x = 3
.long .L2 # x = 4
.long .L6 # x = 5
.long .L6 # x = 6
Jump table
switch(x) {
case 1: // .L3
w = y*z;
break;
case 2: // .L4
w = y/z;
/* Fall Through */
case 3: // .L5
w += z;
break;
case 5:
case 6: // .L6
w -= z;
break;
default: // .L2
w = 2;
}

## Slide 9: Handling Fall-Through
long w = 1;
. . .
switch(x) {
. . .
case 2:
w = y/z;
/* Fall Through */
case 3:
w += z;
break;
. . .
}
case 3:
w = 1;
goto merge;
case 2:
w = y/z;
merge:
w += z;

## Slide 10: Code Blocks (Partial)
.L2: # Default
movl $2, %eax # w = 2
jmp .L8 # Goto done
.L5: # x == 3
movl $1, %eax # w = 1
jmp .L9 # Goto merge
.L3: # x == 1
movl 16(%ebp), %eax # z
imull 12(%ebp), %eax # w = y*z
jmp .L8 # Goto done
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
case 3: // .L5
w += z;
break;
. . .
default: // .L2
w = 2;
}

## Slide 11: Code Blocks (Rest)
.L4: # x == 2
movl 12(%ebp), %edx
movl %edx, %eax
sarl $31, %edx
idivl 16(%ebp) # w = y/z
.L9: # merge:
addl 16(%ebp), %eax # w += z
jmp .L8 # goto done
.L6: # x == 5, 6
movl $1, %eax # w = 1
subl 16(%ebp), %eax # w = 1-z
switch(x) {
. . .
case 2: // .L4
w = y/z;
/* Fall Through */
merge: // .L9
w += z;
break;
case 5:
case 6: // .L6
w -= z;
break;
}

## Slide 12: x86-64 Switch Implementation
.section .rodata
.align 8
.L7:
.quad .L2 # x = 0
.quad .L3 # x = 1
.quad .L4 # x = 2
.quad .L5 # x = 3
.quad .L2 # x = 4
.quad .L6 # X = 5
.quad .L6 # x = 6
Jump Table
Same general idea, adapted to 64-bit code
Table entries 64 bits (pointers)
.L3:
movq %rdx, %rax
imulq %rsi, %rax
ret
switch(x) {
case 1: // .L3
w = y*z;
break;
. . .
}

## Slide 13: IA32 Object Code
Setup
  Label .L2 becomes address 0x8048422
  Label .L7 becomes address 0x8048660
08048410 <switch_eg>:
. . .
8048419: 77 07 ja 8048422 <switch_eg+0x12>
804841b: ff 24 85 60 86 04 08 jmp *0x8048660(,%eax,4)
switch_eg:
. . .
ja .L2 # If unsigned > goto default
jmp *.L7(,%eax,4) # Goto *JTab[x]
Assembly Code
Disassembled Object Code

## Slide 14: IA32 Object Code (cont.)
Jump Table
  Doesn’t show up in disassembled code
  Can inspect using GDB
  gdb switch
  (gdb) x/7xw 0x8048660
    Examine 7 hexadecimal format “words” (4-bytes each)
    Use command “help x” to get format documentation
0x8048660: 0x08048422 0x08048432 0x0804843b 0x08048429
0x8048670: 0x08048422 0x0804844b 0x0804844b

## Slide 15: IA32 Object Code (cont.)
Deciphering Jump Table
0x8048660: 0x08048422 0x08048432 0x0804843b 0x08048429
0x8048670: 0x08048422 0x0804844b 0x0804844b
Address | Value | x
0x8048660 | 0x8048422 | 0
0x8048664 | 0x8048432 | 1
0x8048668 | 0x804843b | 2
0x804866c | 0x8048429 | 3
0x8048670 | 0x8048422 | 4
0x8048674 | 0x804844b | 5
0x8048678 | 0x804844b | 6

## Slide 16: Disassembled Targets
8048422: b8 02 00 00 00 mov $0x2,%eax
8048427: eb 2a jmp 8048453 <switch_eg+0x43>
8048429: b8 01 00 00 00 mov $0x1,%eax
804842e: 66 90 xchg %ax,%ax # noop
8048430: eb 14 jmp 8048446 <switch_eg+0x36>
8048432: 8b 45 10 mov 0x10(%ebp),%eax
8048435: 0f af 45 0c imul 0xc(%ebp),%eax
8048439: eb 18 jmp 8048453 <switch_eg+0x43>
804843b: 8b 55 0c mov 0xc(%ebp),%edx
804843e: 89 d0 mov %edx,%eax
8048440: c1 fa 1f sar $0x1f,%edx
8048443: f7 7d 10 idivl 0x10(%ebp)
8048446: 03 45 10 add 0x10(%ebp),%eax
8048449: eb 08 jmp 8048453 <switch_eg+0x43>
804844b: b8 01 00 00 00 mov $0x1,%eax
8048450: 2b 45 10 sub 0x10(%ebp),%eax
8048453: 5d pop %ebp
8048454: c3 ret

## Slide 17: Matching Disassembled Targets
8048422: mov $0x2,%eax
8048427: jmp 8048453 <switch_eg+0x43>
8048429: mov $0x1,%eax
804842e: xchg %ax,%ax
8048430: jmp 8048446 <switch_eg+0x36>
8048432: mov 0x10(%ebp),%eax
8048435: imul 0xc(%ebp),%eax
8048439: jmp 8048453 <switch_eg+0x43>
804843b: mov 0xc(%ebp),%edx
804843e: mov %edx,%eax
8048440: sar $0x1f,%edx
8048443: idivl 0x10(%ebp)
8048446: add 0x10(%ebp),%eax
8048449: jmp 8048453 <switch_eg+0x43>
804844b: mov $0x1,%eax
8048450: sub 0x10(%ebp),%eax
8048453: pop %ebp
8048454: ret
Value
0x8048422
0x8048432
0x804843b
0x8048429
0x8048422
0x804844b
0x804844b

## Slide 18: Today
Switch Statement
Arrays
Structures

## Slide 19: Array Allocation
Basic Principle
  T A[L];
  Array of data type T and length L
  Contiguously allocated region of L * sizeof(T) bytes
char string[12];
x
x + 12
int val[5];
x
x + 4
x + 8
x + 12
x + 16
x + 20
double a[3];
x + 24
x
x + 8
x + 16
char *p[3];
x
x + 8
x + 16
x + 24
x
x + 4
x + 8
x + 12
IA32
x86-64

## Slide 20: Array Access
Basic Principle
  T A[L];
  Array of data type T and length L
  Identifier A can be used as a pointer to array element 0: Type T*
Reference Type Value
  val[4] int 3
  val int * x
  val+1 int * x + 4
  &val[2] int * x + 8
  val[5] int ??
  *(val+1) int 5
  val + i int * x + 4 i
int val[5];
1
5
2
1
3
x
x + 4
x + 8
x + 12
x + 16
x + 20

## Slide 21: Array Example
Declaration “zip_dig cmu” equivalent to “int cmu[5]”
Example arrays were allocated in successive 20 byte blocks
  Not guaranteed to happen in general
#define ZLEN 5
typedef int zip_dig[ZLEN];
zip_dig cmu = { 1, 5, 2, 1, 3 };
zip_dig mit = { 0, 2, 1, 3, 9 };
zip_dig ucb = { 9, 4, 7, 2, 0 };
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36
zip_dig mit;
0
2
1
3
9
36
40
44
48
52
56
zip_dig ucb;
9
4
7
2
0
56
60
64
68
72
76

## Slide 22: Array Accessing Example
Register %edx contains starting address of array
Register %eax contains array index
Desired digit at 4*%eax + %edx
Use memory reference (%edx,%eax,4)
int get_digit
(zip_dig z, int dig)
{
return z[dig];
}
# %edx = z
# %eax = dig
movl (%edx,%eax,4),%eax # z[dig]
IA32
zip_dig cmu;
1
5
2
1
3
16
20
24
28
32
36

## Slide 23: Array Loop Example (IA32)
# edx = z
movl $0, %eax # %eax = i
.L4: # loop:
addl $1, (%edx,%eax,4) # z[i]++
addl $1, %eax # i++
cmpl $5, %eax # i:5
jne .L4 # if !=, goto loop
void zincr(zip_dig z) {
int i;
for (i = 0; i < ZLEN; i++)
z[i]++;
}

## Slide 24: Today
Switch Statement
Arrays
Structures

## Slide 25: Structure Allocation
struct rec {
int a[3];
int i;
struct rec *n;
};
Concept
  Contiguously-allocated region of memory
  Refer to members within structure by names
  Members may be of different types
Memory Layout
i
a
n
0
12
16
20

## Slide 26: Structure Access
struct rec {
int a[3];
int i;
struct rec *n;
};
IA32 Assembly
# %edx = val
# %eax = r
movl %edx, 12(%eax) # Mem[r+12] = val
void
set_i(struct rec *r,
int val)
{
r->i = val;
}
Accessing Structure Member
  Pointer indicates first byte of structure
  Access elements with offsets
i
a
n
0
12
16
20
r+12
r

## Slide 27: Generating Pointer to Structure Member
movl 12(%ebp), %eax # Get idx
sall $2, %eax # idx*4
addl 8(%ebp), %eax # r+idx*4
int *get_ap
(struct rec *r, int idx)
{
return &r->a[idx];
}
Generating Pointer to Array Element
  Offset of each structure member determined at compile time
  Arguments
    Mem[%ebp+8]: r
    Mem[%ebp+12]: idx
r+idx*4
r
i
a
n
0
12
16
20
struct rec {
int a[3];
int i;
struct rec *n;
};

## Slide 28: Following Linked List
.L17: # loop:
movl 12(%edx), %eax # r->i
movl %ecx, (%edx,%eax,4) # r->a[i] = val
movl 16(%edx), %edx # r = r->n
testl %edx, %edx # Test r
jne .L17 # If != 0 goto loop
void set_val
(struct rec *r, int val)
{
while (r) {
int i = r->i;
r->a[i] = val;
r = r->n;
}
}
C Code
struct rec {
int a[3];
int i;
struct rec *n;
};
i
a
n
0
12
16
20
Element i
Register | Value
%edx | r
%ecx | val

## Slide 29: Structures & Alignment
Unaligned Data
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8
c
i[0]
i[1]
v
p
p+1
p+5
p+9
p+17
struct S1 {
char c;
int i[2];
double v;
} *p;

## Slide 30: Alignment Principles
Aligned Data
  Primitive data type requires K bytes
  Address must be multiple of K
  Required on some machines; advised on IA32
    treated differently by IA32 Linux, x86-64 Linux, and Windows!
Motivation for Aligning Data
  Memory accessed by (aligned) chunks of 4 or 8 bytes (system dependent)
    Inefficient to load or store datum that spans quad word boundaries
    Virtual memory very tricky when datum spans 2 pages
Compiler
  Inserts gaps in structure to ensure correct alignment of fields

## Slide 31: Specific Cases of Alignment (IA32)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, char *, …
  lowest 2 bits of address must be 002
8 bytes: double, …
  Windows (and most other OS’s & instruction sets):
    lowest 3 bits of address must be 0002
  Linux:
    lowest 2 bits of address must be 002
    i.e., treated the same as a 4-byte primitive data type
12 bytes: long double
  Windows, Linux:
    lowest 2 bits of address must be 002
    i.e., treated the same as a 4-byte primitive data type

## Slide 32: Specific Cases of Alignment (x86-64)
1 byte: char, …
  no restrictions on address
2 bytes: short, …
  lowest 1 bit of address must be 02
4 bytes: int, float, …
  lowest 2 bits of address must be 002
8 bytes: double, char *, …
  Windows & Linux:
    lowest 3 bits of address must be 0002
16 bytes: long double
  Linux:
    lowest 3 bits of address must be 0002
    i.e., treated the same as a 8-byte primitive data type

## Slide 33: Satisfying Alignment with Structures
struct S1 {
char c;
int i[2];
double v;
} *p;
Within structure:
  Must satisfy each element’s alignment requirement
Overall structure placement
  Each structure has alignment requirement K
    K = Largest alignment of any element
  Initial address & structure length must be multiples of K
Example (under Windows or x86-64):
  K = 8, due to double element
c
i[0]
i[1]
v
3 bytes
4 bytes
p+0
p+4
p+8
p+16
p+24
Multiple of 4
Multiple of 8
Multiple of 8
Multiple of 8

## Slide 34: Different Alignment Conventions
x86-64 or IA32 Windows:
  K = 8, due to double element
IA32 Linux
  K = 4; double treated like a 4-byte data type
struct S1 {
char c;
int i[2];
double v;
} *p;
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | 4 bytes |  |  |  | v |  |  |  |  |  |  |  | 
p+0 |  |  |  | p+4 |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 
 | c | 3 bytes |  |  | i[0] |  |  |  | i[1] |  |  |  | v |  |  |  |  |  |  |  |  |  |  | 
p+0 |  |  |  | p+4 |  |  |  | p+8 |  |  |  | p+12 |  |  |  |  |  |  | p+20 |  |  |  |  | 

## Slide 35: Meeting Overall Alignment Requirement
For largest alignment requirement K
Overall structure must be multiple of K
struct S2 {
double v;
int i[2];
char c;
} *p;
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
p+0 |  |  |  |  |  |  | p+8 |  |  |  |  |  |  |  | p+16 |  |  |  |  |  |  |  | p+24 | 

## Slide 36: Arrays of Structures
Overall structure length multiple of K
Satisfy alignment requirement for every element
struct S2 {
double v;
int i[2];
char c;
} a[10];
 | v |  |  |  |  |  |  | i[0] |  |  |  | i[1] |  |  |  | c | 7 bytes |  |  |  |  |  |  | 
a+24 |  |  |  |  |  |  | a+32 |  |  |  |  |  |  |  | a+40 |  |  |  |  |  |  |  | a+48 | 
 | a[0] |  |  |  |  | a[1] |  |  |  |  | a[2] |  |  |  |  | • • • |  |  |  |  |  | 
a+0 |  |  |  |  | a+24 |  |  |  |  | a+48 |  |  |  |  | a+72 |  |  |  |  |  |  | 

## Slide 37: Accessing Array Elements
Compute array offset 12i
  sizeof(S3), including alignment spacers
Element j is at offset 8 within structure
Assembler gives offset a+8
  Resolved during linking
struct S3 {
short i;
float v;
short j;
} a[10];
short get_j(int idx)
{
return a[idx].j;
}
# %eax = idx
leal (%eax,%eax,2),%eax # 3*idx
movswl a+8(,%eax,4),%eax
 | a[0] |  |  |  |  | • • • |  |  |  | a[i] |  |  |  | • • |  |  | • |  |  | 
a+0 |  |  |  |  | a+12 |  |  |  | a+12i |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  | i |  | 2 bytes |  | v |  |  |  | j |  | 2 bytes |  |  | 
 |  |  |  |  | a+12i |  |  |  |  |  |  |  | a+12i+8 |  |  |  |  |  | 

## Slide 38: Saving Space
Put large data types first
Effect (K=4)
struct S4 {
char c;
int i;
char d;
} *p;
struct S5 {
int i;
char c;
char d;
} *p;
c
i
3 bytes
d
3 bytes
c
i
d
2 bytes